## Slide 1: QUESTIONS?
Operations
  how many?
  which ones
Operands
  how many?
  Location
  Types
  how to specify?
instruction format
  Size
  how many formats?
  how does the computer know what0001 0100 1101 1111means?
ALL ABOVE SPECIFY DESIGN OF INSTRUCTIONS

## Slide 2: INSTRUCTION SET ARCHITECTURE
HOW TO TALK WITH COMPUTER ?
PROVIDES COMMAND TO THE PROCESSOR
WHAT IS CONSISTS OF ?
  addressing modes
  instructions
  native data types
  Registers
  memory architecture
  Interrupt
  exception handling
  external I/O.

## Slide 3: GOAL
EASINESS FOR PROGRAMMER
  Designing an ISA is to make a CPU which has enough functionality so that programmers can write programs for it.
we need instructions to do basic maths, data comparisons, deal with data of different sizes, and instructions to branch and jump.
There are an infinite number of ways we can build instruction sets to achieve the above.

## Slide 4: WHAT ISSUES ISA IS GOING TO HANDLE?
Registers
Bus Sizes
Operations
How Many Operands?
Instruction Format

## Slide 5: EXAMPLE
Let's design an ISA with 8 registers, a 16-bit data bus and word size, and a 24-bit address bus: quite suitable for an embedded CPU, e.g. in a microwave or engine control system.

## Slide 6: TYPES OF ISA
CISC
RISC

## Slide 7: TYPES OF ISA
CISC
RISC

## Slide 8: CISC
WHAT MEANS TO COMPLEX?  EASINESS FOR PROGRAMMER
  ISA designers created instruction sets with instructions to do everything, and the instructions themselves performed complex operations. Instruction sets of this type are now known as CISC architectures.
  CISC ISAs made writing programs in assembly much easier for the programmers.
NUMBER OF MEMORY ACCESS
  number of memory accesses to perform a CISC instruction can vary from 1 (instruction fetch) to several.
EXECUTION TIME
  This implies that CISC instructions take variable amounts of time to execute, depending on their complexity and the number of memory accesses required

## Slide 9: RISC
WHAT MEANS TO REDUCE?
  It does not mean that the number of operations was reduced (although this did happen), but that the instructions available performed simpler tasks
  instructions were simpler, there were more registers, the number of addressing modes was reduced
FOR PROGRAMMER?
EXECUTION TIME ?

## Slide 10: MIPS ISA
RISC OR CISC?

## Slide 11: MIPS ISA
DATA BUS AND ADDRESS BUS
  The data bus size (and the word size) is 32 bits, and the address bus is 32 bits too.
DATA TYPES
  MIPS supports 4 integer data types: 8-bit bytes, 16-bit halfwords, 32-bit words and 64-bit doublewords.
FLOATING POINT
  Floating point types are also supported: 32-bit single-precision and 64-bit double-precision values.
REGISTERS
  MIPS provides 32 general-purpose 32-bit registers, although the operating system, assembler and libraries reserve some of these for special use.

## Slide 12: INSTRUCTIONS IN MIPS
load registers with values, either from RAM or with literal values.
store register values (i.e. copy them) out to RAM locations.
basic integer arithmetic: add, subtract, multiply, divide with remainder.
basic floating-point arithmetic: add, subtract, multiply, divide.
logical operations: AND, OR, NOR, exclusive OR (XOR).
shift operations: shift left, shift right.
comparison operations: ==, !=, <, >, <=, >=
instructions to change the flow of control: relative branches and jumps.

## Slide 13: INSTRUCTION FORMAT
R-type instructions, which perform arithmetic and logical operations on registers.
I-type instructions, which deal with load/stores and immediate literal values, as well as branches.
J-type instructions, which are used for jumps and function calls.

## Slide 14: R-TYPE VS I-TYPE VS J-TYPE

## Slide 15: MIPS ASSEMBLY INSTRUCTIONS

## Slide 16: FIRST PROGRAM IN MIPS ASSEMBLY

## Slide 17: .DATA, .TEXT, & .GLOBL Directives
.DATA directive
  Defines the data segment of a program containing data
  The program's variables should be defined under this directive
  Assembler will allocate and initialize the storage of variables
.TEXT directive
  Defines the code segment of a program containing instructions
.GLOBL directive
  Declares a symbol as global
  Global symbols can be referenced from other files
  We use this directive to declare main procedure of a program

## Slide 18: System Calls
Programs do input/output through system calls
MIPS provides a special syscall instruction
  To obtain services from the operating system
Using the syscall system services
  Load the service number in register $v0
  Load argument values, if any, in registers $a0, $a1, etc.
  Issue the syscall instruction
  Retrieve return values, if any, from result registers

## Slide 19: Syscall Services
Service | $v0 | Arguments / Result
Print Integer | 1 | $a0 = integer value to print
Print Float | 2 | $f12 = float value to print
Print Double | 3 | $f12 = double value to print
Print String | 4 | $a0 = address of null-terminated string
Read Integer | 5 | Return integer value in $v0
Read Float | 6 | Return float value in $f0
Read Double | 7 | Return double value in $f0
Read String | 8 | $a0 = address of input buffer $a1 = maximum number of characters to read
Allocate Heap memory | 9 | $a0 = number of bytes to allocate Return address of allocated memory in $v0
Exit Program | 10 | 

## Slide 20: Syscall Services – Cont’d
Print Char | 11 | $a0 = character to print
Read Char | 12 | Return character read in $v0
Open File | 13 | $a0 = address of null-terminated filename string $a1 = flags (0=read, 1=write, 9=append) $a2 = mode (ignored) Return file descriptor in $v0 (negative if error)
Read from File | 14 | $a0 = File descriptor $a1 = address of input buffer $a2 = maximum number of characters to read Return number of characters read in $v0
Write to File | 15 | $a0 = File descriptor $a1 = address of buffer $a2 = number of characters to write Return number of characters written in $v0
Close File | 16 | $a0 = File descriptor

## Slide 21: Reading and Printing an Integer
################# Code segment #####################
.text
.globl main
main: # main program entry
li $v0, 5 # Read integer
syscall # $v0 = value read
move $a0, $v0 # $a0 = value to print
li $v0, 1 # Print integer
syscall
li $v0, 10 # Exit program
syscall

## Slide 22: Reading and Printing a String
################# Data segment #####################
.data
str: .space 10 # array of 10 bytes
################# Code segment #####################
.text
.globl main
main: # main program entry
la $a0, str # $a0 = address of str
# (note: la is a pseudo instruction)
li $a1, 10 # $a1 = max string length
li $v0, 8 # read string
syscall
li $v0, 4 # Print string str
syscall
li $v0, 10 # Exit program
syscall

## Slide 23: YOUR TASK
WRITE A PROGRAM IN MIPS ASSEMBLY TO TAKE THREE INTEGERS FROM USER AND STORE THEIR SUM ON SCREEN.