## Slide 1: Conditional Processing
COE 205
Computer Organization and Assembly Language
Dr. Aiman El-Maleh
College of Computer Sciences and Engineering
King Fahd University of Petroleum and Minerals
[Adapted from slides of Dr. Kip Irvine: Assembly Language for Intel-Based Computers]

## Slide 2: Next . . .
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Translating Conditional Structures
Indirect Jump and Table-Driven Selection
Application: Sorting an Integer Array

## Slide 3: Block-Structured IF Statements
IF statement in high-level languages (such as C or Java)
  Boolean expression (evaluates to true or false)
  List of statements performed when the expression is true
  Optional list of statements performed when expression is false
Task: Translate IF statements into assembly language
Example:
  mov eax,var1
  cmp eax,var2
  jne elsepart
  mov X,1
  jmp next
elsepart:
mov X,2
next:
if( var1 == var2 )
X = 1;
else
X = 2;

## Slide 4: Your Turn . . .
Translate the IF statement to assembly language
All values are unsigned
  cmp ebx,ecx
  ja next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx )
{
eax = 5;
edx = 6;
}
There can be multiple correct solutions

## Slide 5: Your Turn . . .
Implement the following IF in assembly language
All variables are 32-bit signed integers
  mov eax,var1
  cmp eax,var2
  jle ifpart
  mov var3,6
  mov var4,7
  jmp next
ifpart: mov var3,10
next:
if (var1 <= var2) {
var3 = 10;
}
else {
var3 = 6;
var4 = 7;
}
There can be multiple correct solutions

## Slide 6: Compound Expression with AND
HLLs use short-circuit evaluation for logical AND
If first expression is false, second expression is skipped
if ((al > bl) && (bl > cl)) {X = 1;}
; One Possible Implementation ...
cmp al, bl ; first expression ...
ja L1 ; unsigned comparison
jmp next
L1: cmp bl,cl ; second expression ...
ja L2 ; unsigned comparison
jmp next
L2: mov X,1 ; both are true
next:

## Slide 7: Better Implementation for AND
cmp al,bl ; first expression...
jbe next ; quit if false
cmp bl,cl ; second expression...
jbe next ; quit if false
mov X,1 ; both are true
next:
The following implementation uses less code
By reversing the relational operator, We allow the program to fall through to the second expression
Number of instructions is reduced from 7 to 5
if ((al > bl) && (bl > cl)) {X = 1;}

## Slide 8: Your Turn . . .
Implement the following IF in assembly language
All values are unsigned
  cmp ebx,ecx
  ja next
  cmp ecx,edx
  jbe next
  mov eax,5
  mov edx,6
next:
if ((ebx <= ecx) &&
(ecx > edx))
{
eax = 5;
edx = 6;
}

## Slide 9: Application: IsDigit Procedure
IsDigit PROC
cmp al,'0' ; AL < '0' ?
jb L1 ; yes? ZF=0, return
cmp al,'9' ; AL > '9' ?
ja L1 ; yes? ZF=0, return
test al, 0 ; ZF = 1
L1: ret
IsDigit ENDP
Receives a character in AL
Sets the Zero flag if the character is a decimal digit
if (al >= '0' && al <= '9') {ZF = 1;}

## Slide 10: Compound Expression with OR
HLLs use short-circuit evaluation for logical OR
If first expression is true, second expression is skipped
Use fall-through to keep the code as short as possible
if ((al > bl) || (bl > cl)) {X = 1;}
cmp al,bl ; is AL > BL?
ja L1 ; yes, execute if part
cmp bl,cl ; no: is BL > CL?
jbe next ; no: skip if part
L1: mov X,1 ; set X to 1
next:

## Slide 11: WHILE Loops
while( eax < ebx) { eax = eax + 1; }
A WHILE loop can be viewed as
IF statement followed by
The body of the loop, followed by
Unconditional jump to the top of the loop
top: cmp eax,ebx ; eax < ebx ?
jae next ; false? then exit loop
inc eax ; body of loop
jmp top ; repeat the loop
next:
This is a possible implementation:

## Slide 12: Your Turn . . .
top: cmp ebx,var1 ; ebx <= var1?
ja next ; false? exit loop
add ebx,5 ; execute body of loop
dec var1
jmp top ; repeat the loop
next:
while (ebx <= var1) {
ebx = ebx + 5;
var1 = var1 - 1
}
Implement the following loop, assuming unsigned integers

## Slide 13: Yet Another Solution for While
cmp ebx,var1 ; ebx <= var1?
ja next ; false? exit loop
top: add ebx,5 ; execute body of loop
dec var1
cmp ebx, var1 ; ebx <= var1?
jbe top ; true? repeat the loop
next:
while (ebx <= var1) {
ebx = ebx + 5;
var1 = var1 - 1
}
Check the loop condition at the end of the loop
No need for JMP, loop body is reduced by 1 instruction

## Slide 14: Next . . .
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Translating Conditional Structures
Indirect Jump and Table-Driven Selection
Application: Sorting an Integer Array

## Slide 15: Indirect Jump
Direct Jump: Jump to a Labeled Destination
  Destination address is a constant
    Address is encoded in the jump instruction
    Address is an offset relative to EIP (Instruction Pointer)
Indirect jump
  Destination address is a variable or register
    Address is stored in memory/register
    Address is absolute
Syntax: JMP mem32/reg32
  32-bit absolute address is stored in mem32/reg32 for FLAT memory
Indirect jump is used to implement switch statements